## Slide 1: AST10401 Introduction to Electrical Engineering
1. Basic Concepts and Laws in Electrical Engineering

## Slide 2: Charge(電荷)
All matter is made of atoms.
Each atom is made of electron(s), proton(s) and neutron(s).
Both proton and electron carry charges.
Charge is a fundamental electric quantity which is measured in Coulombs (C).
The Atomic Model of an atom

## Slide 3: Charge
Each proton carries the amount of +ve charge q0 = +1.60210-19 C.
Each electron carries the amount of –ve charge -q0 = -1.60210-19 C.
Like charges repel each other.
Opposite charges attract each other.
Charges found in nature are usually integral multiples of q0. (i.e. +/- q0, +/- 2q0 , +/- 3q0)

## Slide 4: Electric Current(電流)
Electric Current (i)
The amount of positive charges passing through a given cross section of
a substance in one second is called Electric Current.
The unit of Current :
1 Ampere (A) = 1 Coulomb/second
  dq charge that flow through a given cross-sectional area in dt units of time.

## Slide 5: Electric Current
The direction of current is defined as the flow direction of +ve charges.
1C +ve charges flow from Right to Left per second, so there is 1A current flows from Right to Left.
L
R

## Slide 6: Electric Current
1C -ve charges flow from Left to Right per second, so there is 1A current
flows from Right to Left.
The direction of current can also be defined as the opposite direction of -ve charges flow.
L
R

## Slide 7: Electric Current
Positive charges
Negative charges
=
L
R
1C +ve charges flow from R to L per second
= 1C -ve charges flow from L to R per second
= 1A current flows from Right to Left.

## Slide 8: Electric Current
Example
A conductor has a constant current of 5 A. How many electrons pass a cross section of the conductor in one minute?
Solution
Total no. of charges pass in 1 min in 5 A current = (5 C/s) (60) = 300 C/min
Total no. of electrons pass in 1 min is given by
5A
L
R

## Slide 9: Electric Potential Energy
In electrical engineering, moving charges in a substance involves some work or electric potential energy (電勢能) transferred(gain/loss).
We simply call electric potential energy as “energy” in this course.
The work or energy is measured in joules(J).

## Slide 10: Voltage(電壓)
  10
Voltage at Point a (Va)
The energy transferred (gain/loss) of a unit +ve charge (+1C) moving from a reference point to point a in an electric element.
The unit of voltage is Volt(V).
The voltage at a reference point is defined as 0V.
A reference point defined as 0V
a
b
Va
Consider a 1C +ve charge moves from a reference point (0V) to point a,
if it gains 2J energy, then Va = +2V.
If it losses 2J energy, then Va = -2V.
1C
The unit of energy is Joules (J)

## Slide 11: Voltage Difference
Potential/Voltage Difference between points a and b in an electric element, Vab is defined as
Vab is also called as Voltage Across point a and point b in an element.
It is found that Vab is related to energy transferred:
DWba is the energy transfer of charges q moving from b to a.
a
b
Vb
Va
q
Vab

## Slide 12: Voltage Difference
Find the energy transferred of +2C moving from b to a via the element below.
Given q = +2C, Va = 10V and Vb = 5V,
Vab = Va – Vb = 10 – 5 = 5V,
As Vab = DWba / q , so DWba = 5 (+2) = +10J.
That means when +2C charge moves from b to a, the charge gains 10J.
(+ve means a gain)
b
a
a reference point with 0V
+2C
5V
10V
DWba

## Slide 13: Voltage Difference
Find the energy transferred of +2C moving from b to a via the element below.
Given q = +2C, Va = 5V and Vb = 10V,
Vab = 5 – 10 = -5V,
As Vab = DWba / q , so DWba = -5 (+2) = -10J.
That means when +2C charge moves from b to a, the charge losses 10J.
(-ve means a loss)
b
a
+2C
a reference point with 0V
10V
5V
DWba

## Slide 14: Voltage Difference
Given that there is a voltage across an element, the terminal with a higher voltage is marked with a + sign and the terminal with a lower voltage is marked with a - sign

## Slide 15: Power(功率)
When a charge passes through an electric element, energy transferred takes place between the charge and element.
Power (p) of an element:
The energy transferred of the element per second in watts (W). Mathematically:
where v is the voltage across the element and i is the current.
The change of energy content of the element in one second

## Slide 16: Power(功率)
Power (p) of an element: the energy transferred of the element per second
Case 1: (the current entering point has a higher voltage then leaving point)
+ve charges loss power
2) the power absorbed by the element
3) The power of the element increases
4) The element’s power is defined as +ve:
p = +|v||i|
a current / a charge flows from a to b
a
b
+2C
10V
5V
+ve sign represents power absorption of an element
charge losses energy

## Slide 17: Power(功率)
Power (p) of an element: the energy transferred of the element per second
Case 2: (the current entering point has a lower voltage)
-ve sign represents power supplying of an element
a current / a charge flows from b to a
a
b
b
a
+2C
5V
10V
charge gains energy
+ve charges gain power
2) the power supplied by the element
3) the power of the element decreases
4) the element’s power is defined as -ve:
p = -|v||i|

## Slide 18: Power
+
v
_
i
p = +|v||i|
+
v
_
i
p = -|v||i|
a
b
a
b
Voltage at the current entering point > voltage at the current leaving point
Voltage at the current entering point < voltage at the current leaving point
Power Absorbing Element with +ve power
Power Supplying Element with –ve power

## Slide 19: Power Sum
In an electric circuit, Total Power supplied = Total Power absorbed
According to the previous definitions, at any time we have:
Sum of all power in a circuit must be zero.

## Slide 20: Power Sum
Example:
Now V1 = Vab = 1.5V
Power of the light bulb = +|V1|x|I| = +|1.5|x|2| = +3W
Power of the battery = -|Vab|x|I| = -|1.5|x|2| = -3W
+
_
1.5 V
I = 2A
I
v1
a
b
vab
+
+
_
_
The battery
supplies power
The light bub
absorbs power

## Slide 21: Electrical Sources
An electrical source is a device that is capable of converting non-electric energy to electric energy.
e.g.:
A battery: Chemical Energy to Electric Energy
An electric generator: Mechanical Energy to Electric Energy

## Slide 22: Electrical Sources
There are 4 types of source in electrical engineering.
  Independent Voltage Sources
  Dependent Voltage Sources
  Independent Current Sources
  Dependent Current Sources

## Slide 23: Independent Voltage Sources
Independent Voltage Source:
A circuit element that maintains a certain voltage across its terminals, regardless of the current flowing inside.
Device symbols:
  Voltage is known, but its current is determined by the electrical elements that are connected to the source.
A battery is considered as an independent voltage source.

## Slide 24: Dependent Voltage Sources
The voltage of a source depends on a voltage or current somewhere else in the circuit.
Device symbols:
v =m vx
v =r ix
Voltage-Controlled
Voltage Source (VCVS)
Current-Controlled
Voltage Source (CCVS)
depends on other voltage Vx
depends on other
current ix

## Slide 25: Independent Current Sources
Independent Current Source:
A circuit element that maintains a certain current through its terminals, regardless of the voltage across those terminals.
Device symbols:
  Current is known, but its voltage is determined by the electrical elements that are connected to the source.

## Slide 26: Dependent Current Sources
The current of a source depends on a voltage or current somewhere else in the circuit.
Device symbols:
i =a vx
i =a ix
Voltage-Controlled
Current Source (VCCS)
Current-Controlled
Current Source (CCCS)
depends on other voltage Vx
depends on other voltage ix

## Slide 27: Ground
Ground: represents a specific reference node.
Usually assign 0V to ground
The ground symbol:

## Slide 28: Resistors
Resistor:
A 2-termainal power absorbing device that its current and voltage across the 2 terminals are determined by Ohm’s law.
Device symbols:

## Slide 29: Ohm’s Law
Ohm’s law
The voltage across a resistor is directly proportional to the current
flowing through the resistor.
The mathematical expression for Ohm’s Law is as follows:
where R is a constant and called resistance, measured in Ohm(W).
Va
Vb
R
I
+
-
current from a to b
a
b
A resistor is a power absorbing device.

## Slide 30: Ohm’s Law
The i-v characteristic curve of a resistor
I
V
Va
Vb
R
I
+
-
current from a to b
a
b

## Slide 31: Ohm’s Law
Given that Va = 10V, Vb = 5V and I = 1A, Find R
Vab = Va – Vb = 10 – 5 = 5V
By Ohm’s law: R = Vab / I = 5W
Va
Vb
Vab
R
+
-
I

## Slide 32: Ohm’s Law
The power absorbed by a resistor:
Va
Vb
Vab
R
+
-
I