## Slide 1: AST10401 Introduction to Electrical Engineering
L02 Electric Circuits

## Slide 2: Electric Circuits
An electric circuit is a connection of electric elements with wires and those electric elements are usually connected to form loop(s).
A loop is a closed path. (i.e. a journey starts and ends at the same point.)
R1
V
+
_
R2
R3
an electric circuit
a conductive wire with zero resistance

## Slide 3
Circuit Terminologies

## Slide 4: Branches
A branch is an element in a circuit. (e.g. a voltage source or a resistor)
R1
V
+
_
R2
R3
R1
V
+
_
R2
R3
4 branches in this circuit

## Slide 5: Nodes
A node in a circuit is a point that joins branches together.
V
+
_
R1
R2

## Slide 6
A circuit containing 3 nodes
If nodes are joined together by wire(s) only, those nodes are considered as the same node.
Nodes and Branches

## Slide 7: Nodes and Branches
Example
How many branches and nodes are there?
5 Branches and 3 nodes
original circuit
equivalent circuit

## Slide 8
Laws in Circuit Theory

## Slide 9: Kirchhoff’s Current Law
Kirchhoff’s Current Law (KCL):
The algebraic sum of currents at a node is zero.
Define:
A current entering a node has +ve sign.
A current leaving a node has –ve sign.
Mathematically,
signs of numbers are taken into account
sum of “in” = sum of “out”
KCL helps form a current relationship.
-ve
+ve

## Slide 10: KCL
Example: Find i0 and i4
is = 5A, i1 = 2A, i2 = 3A, i3 = 1.5A
+
_
Vs
is
i0
i1
i2
i3
i4
a
c
b
i4 flows in the opposite way to the early assumption.
2A
3A
1.5A
5A
-ve
+ve
you can make an assumption on the flow direction of an unknown current initially.
is

## Slide 11: Kirchhoff’s Voltage Law
Kirchhoff’s Voltage Law (KVL):
The algebraic sum of all voltage/potential differences around a loop in a circuit is zero.
Summing clock-wisely or anti-clock-wisely is the same.
Mathematically,
By the conservation of energy
KVL helps form a voltage relationship.

## Slide 12: KVL
The way to sum:
1) Start at any node in the loop, move clock-wisely (a → b → c → d → e →a).
2) Summing the potential difference of each element in the loop gives 0.
3) When we enter an element and leave it with a voltage drop, the potential difference of that element is +ve.
4) When we enter an element and leave it with a voltage gain, the potential difference of that element is -ve.
a
b
c
d
e
b
a
+ v -
move from a to b:
a voltage drop by v, so +v
move from b to a:
a voltage gain by v, so -v

## Slide 13: KVL
Example
Start at a and sum clock-wisely (a → b → c → d → e → a)
By KVL, we have:
(V2) + (V3) + (-V4) + (V5) + (-V1) = 0
So V2 + V3 +V5 = V1 + V4
a
b
c
d
e
b
a
+ v -
move from a to b:
a voltage drop by v, so +v
move from b to a:
a voltage gain by v, so -v
-
+

## Slide 14: KVL
Example:
Find v2 given that vs = 12V, v1 = 6V, v3 = 1V
Vs
+
_
+ v1 –
+
v3
–
+ v2 –
a
b
c
d
(a → b → c → d → a)

## Slide 15
Combining resistors

## Slide 16: Resistors in Series
For N resistors connected in series (N resistors connected as a chain), we have
R1
∙ ∙ ∙
∙ ∙ ∙
R2
R3
Rn
RN
Req
All resistors connected in series are having the same current.

## Slide 17: Voltage Divider
R1 and R2 are in series
Req = R1 + R2
i = v / Req
By Ohm’s law,
v1 = i R1 and v2 = i R2
If R1 is larger than R2, V1 will get a larger share of V.
equivalent circuit

## Slide 18: Voltage Divider
The previous result can be extended. If we have N resistors connected in series, voltage across Ra would be:
R1
∙ ∙ ∙
∙ ∙ ∙
R2
R3
Ra
RN
V
+
_
+ V1 -
+ V2 -
+ VN -
+ Va -

## Slide 19: Voltage Divider
Example

## Slide 20: Resistors in Parallel
For N resistors connected in parallel (they are connected together by two nodes only), we have
R1
R2
R3
RN
Req
All resistors connected in parallel are having the same voltage.

## Slide 21: Current Divider
As R1 and R2 are in parallel, voltage drops are the same.
i1
i2
R1
i
R2
+
v
–
a
i
Req
i
+
Vx
–
If R1 is very large, i2 gets a large share of i.
i
i
Equivalent circuit

## Slide 22: Current Divider
The previous result can be extended. If N resistors are connected in parallel, current flow in Ra would be:
R1
R2
R3
Ra
RN
i
where
i
Req
i
ia

## Slide 23: Current Divider
Example: Find i1

## Slide 24: Find i1, i2 and i3
Req1
Example

## Slide 25: Find i2 and i3
Now we know i1 = 3A,
As a voltage divider,
By Ohm’s law:
Voltage across R2 = Voltage across Req