## Slide 1: AST10401 Introduction to Electrical Engineering
03. Circuit Analysis II

## Slide 2: If you are given the following circuit, can you determine the voltage across 4W resistor simply by inspection?
Analyzing circuit by inspection?

## Slide 3: Linearity
Linearity of an electric element is a special relationship between the voltage and current of the electric element.
The concept of linearity is a combination of Scaling Property and Additive Property.
Scaling Property: if a current of an electric element is multiplied by a constant, its corresponding voltage is multiplied by the same constant.
Additive Property: the voltage of an electric element due to a current sum equals the sum of voltages due to each current applied separately.

## Slide 4: Scaling Property
Assume that we applied a current I to a resistor, we have voltage V across its terminals where V = IR, by Ohm’s law.
If we have a new current I’ = kI, where k is a constant, then we have a new voltage V’ developed and it is given by V’ = kV.
So a resistor has Scaling Property.
V
R
+
-
I
V’ = I’R = (kI)R = k(IR) = kV
R
+
-
I’ = kI
V’
V = IR

## Slide 5: Additive Property
Given that two currents I1 and I2 , then V1 = I1R and V2 = I2R.
Applying I3 = I1 + I2 to the resistor, we have
It shows a resistor has Additive Property, hence a resistor is a linear element.
V1
R
+
-
V2
R
+
-
I2
I1
v3
R
+
-
I3
V3 = I3R
= (I1 + I2)R = I1R + I2R
= V1 + V2
V3 = Sum of the voltages due to I1 and I2

## Slide 6: Linearity Property
If an electric circuit consists of only linear elements, linear dependent sources and independent sources, then the electric circuit is called a linear electric circuit.
If all sources are scaled by a constant k, all the currents and voltages will be scaled by the same k as well.
If is = 15A and vo = 20V
If is = 30A (k=2), by the linear property of an electric circuit,
vo = 20 x 2 = 40V

## Slide 7: Superposition Principle
Superposition Principle
The current/voltage of an element in a Multiple Sources Linear Circuit can be determined by 2 steps:
1) First obtaining the current/voltage of that element due to each independent source working alone.
2) Summing up all those currents/voltages found in 1) to get the answer.
By Superposition, v = v1 + v2
where
v1 is the voltage across 4W due to the 6V working alone
v2 is the voltage across 4W due to the 3A working alone.

## Slide 8: Superposition Principle
How to make one independent source works alone in a circuit?
By switching off all the rest of independent sources:
When setting voltage sources to zero they become short circuits (v = 0)
v
+
–
When setting current sources to zero they become open circuits (i = 0)
i

## Slide 9: Superposition Principle
Example:
By Superposition, v = v1 + v2
where
v1 is the voltage across 4W due to the 6V voltage source working alone
v2 is the voltage across 4W due to the 3A current source working alone.

## Slide 10: Superposition Principle
Find v1 by the voltage divider rule:

## Slide 11: Superposition Principle
Find v2 by the current divider rule:

## Slide 12: Superposition Principle
Adding the two results:

## Slide 13: Superposition Principle
Example:
Find vx in the circuit below.
Dependent source keep unchanged

## Slide 14: Superposition Principle
2A is discarded by open-circuit
20 
v1
4 
10 V
+

(a)
0.1v1
4 
2 A
(b)
20 
0.1v2
v2
10V is discarded by short-circuit
Dependent source keep unchanged

## Slide 15: Thevenin’s Theorem
Thevenin’s Theorem
Any two terminal linear circuit can be replaced by an equivalent circuit which is a voltage source VTh connects in series with a resistor RTh .
How to find Thevenin voltage VTh and Thevenin resistance RTh?

## Slide 16: Thevenin’s Theorem
Finding VTh :
VTh can obtained by calculating or measuring the voltage across the two terminals of the original linear circuit.
+
Vab
-
Vab = VTh
a
b

## Slide 17: Thevenin’s Theorem
Finding RTh:
1) Turning off all sources in the circuit
2) Applying a test voltage source vo (known) across a and b.
3) Finding io drawn from vo.
4) RTh = vo / io

## Slide 18: Thevenin’s Theorem
If there is no dependent sources in the linear circuit,
then RTh is the equivalent resistance “seen” from the terminals a-b when all the independent sources are turned off.
a
b
Rin is the equivalent resistance across a and b when all independent sources inside are turned off.
Rin
Rin = RTH

## Slide 19: Thevenin’s Theorem
Example
Find the Thevenin equivalent of the circuit shown below to the left of the terminals a-b. Then find the current through RL = 6W

## Slide 20: Thevenin’s Theorem
Find RTh by turning off the 32V voltage source and 2A current source:
RTH = (4 || 12) + 1 = 4 W

## Slide 21: Thevenin’s Theorem
Find VTh. We consider the circuit below.
Note that Vc = Va (why?), so VTh = Vab = Vcb. Apply superposition:
c

## Slide 22: Thevenin’s Theorem
Find the current through RL = 6W
IL = 30 / (4 + 6) = 3A
IL

## Slide 23: Thevenin’s Theorem
Example
Find the Thevenin equivalent of the circuit shown below to the left of the terminals a-b.
6 V
5 
Ix
4 
+

1.5Ix
3 
o
+
VTh

b
a
1.5Ix
1 V
+

3 
5 
a
b
4 
Ix
i
Find vTh
Find RTh

## Slide 24: Thevenin’s Theorem
Ix = i2
1.5 Ix = i2 – i1
i1 = -0.5 i2 (1)
For the Supermesh:
5 i1 + 3 i2 + 4 i2 - 6 = 0
6 = 5 i1 + 7 i2 (2)
Solving (1) and (2), we have
i2 = 4/3 A
So VTh = 4 (4/3) = 5.33V
c
d

## Slide 25: Thevenin’s Theorem
Turn off the 6V and apply a test voltage 1V across a and b to find i:
1.5Ix = Ix + 0.5Ix
+
-
+
-
c
I4W

## Slide 26: Norton’s Theorem
Norton’s Theorem
Any two terminal linear circuit can be replaced by an equivalent circuit
which is a current source IN connects in parallel with a resistor RN .
How to find Norton current IN and Norton resistance RN?
the Norton equivalent to the two-terminal linear circuit

## Slide 27: Norton’s Theorem
Finding IN
The Norton current IN is the short-circuit current at the terminal of the linear circuit.

## Slide 28: Norton’s Theorem
Finding RN
1) Turning off all sources in the circuit
2) Applying a test voltage source vo (known) across a and b.
3) Finding io drawn from vo.
4) RN = vo / io
Refer back to Thevenin theorem,
RN = RTh

## Slide 29: Norton’s Theorem
If there is no dependent sources in the linear circuit,
then RN is the equivalent resistance “seen” from the terminals a-b when all the independent sources are turned off.
a
b
Rin is the equivalent resistance across a and b when all independent sources inside are turned off.
Rin
Rin = RN = RTH

## Slide 30: Norton’s Theorem
Example: Find the Norton equivalent of the following circuit at terminal a-b
RN = 6 || 6 = 3W

## Slide 31: Norton’s Theorem
IN
At node c, by KCL
(15 – Vc) /3 + 4 = IN (1)
Vc / 3 = IN (2)
Solve for IN in (1) and (2),
we have IN = 4.5 A
c
0V
RN = 3W
4.5 A

## Slide 32: Source Transformation
Given the following voltage source and resistor pair (Thevenin equivalent), we can always find its Norton equivalent:
where
IN = vs /R (by shorting the a and b in the original configuration)
RN = R (by turning off vs and see from terminal a-b)
RN
IN

## Slide 33: Source Transformation
Given the following current source and resistor pair (Norton equivalent), we can always find its Thevenin equivalent:
RTh
VTh
where
VTh = is x R (by measuring the voltage across a and b)
RTh = R (by turning off is and see from terminal a-b)

## Slide 34: Source Transformation
Example: Find vo
12 = 3 X 4

## Slide 35: Source Transformation

## Slide 36: Source Transformation
By current divider:
i = 2 (2/(2+8))
Vo = 8 i = 3.2V

## Slide 37: Maximum Power Transferred
Find RL such that RL receives maximum power transferred from the 2 terminal linear circuit.
?

## Slide 38: Maximum Power Transferred
If the entire circuit is replaced by its Thevenin equivalent excluding the load, the power delivered to the load is:
The power transfer profile with different RL
For maximum power dissipated in RL, Pmax, for a given RTH and VTH,
any linear circuit

## Slide 39: Maximum Power Transferred
Example:
Find RL for maximum power transfer and the corresponding power

## Slide 40: Maximum Power Transferred
First find the Thevenin equivalent across a and b:
RTh = (6 || 12) + (3 + 2) = 9W

## Slide 41: Maximum Power Transferred
Find VTh:
6i1 + 12i1 - 12i2 - 12 = 0 (1)
i2 = -2A (2)
So i1 = -2/3 A
12 - i1(6) - i2 (3) = VTh
12 - (-2/3)(6) - (-2)(3) = VTh
VTh = 22 V
c
d
b
e

## Slide 42: Maximum Power Transferred
To have a maximum power transfer, we should have RL = RTh = 9W
So