## Slide 1: AST10401 Introduction to Electrical Engineering
4. Capacitors and Inductors

## Slide 2: Capacitors
A capacitor is a device that consists of two metal plates separated by an insulator/dielectric (air, ceramic or mica).
A capacitor is an electrical element designed to store energy.
Electrical Symbol

## Slide 3: Capacitors
Inside metal, only electrons are free to move as charge carriers.
When we apply a voltage source v across a capacitor, the source attracts electrons on the metal plate connected to the +ve terminal of the source and put them on the metal plate connected to the –ve terminal of the source.
When an electron leaves, it leave behind a +ve charge.
+
v
+
–
an open circuit, no constant current flow at the end
e-

## Slide 4: Capacitors
When a voltage source v is applied long enough (at steady state), there are fixed amount of positive charges q developed on one plate and there are fixed amount of negative charges –q on the other.
We have charge separation across the plates and it is due to the voltage source.
+
+
+
+
–
–
–
–
–
v
+
–
q
-q

## Slide 5: Capacitors
The amount of charge q stored in the capacitor is proportional to the applied voltage v:
C is a constant and known as the capacitance.
Capacitance is measured in farad (F), 1 Farad = 1 Coulomb / Volt
The capacitance C of a capacitor depends on its dimensions:
d
A
Dielectric (or air)
ε – relative permittivity
(dielectric constant)

## Slide 6: Capacitors
To obtain the current-voltage relationship of a capacitor, consider
and differentiate both side of , we have
The voltage-current relationship can be obtained by integrating both side
of the above relationship:
initial voltage
at t = t0

## Slide 7: Capacitors
The capacitor is an electric energy storing device.
The energy w stored in the capacitor is given by
Since there is an insulator between the two plates, you expected that there is no current flow at the end even you continuously apply a voltage source.
A capacitor is an open circuit at steady state (i.e. dv/dt = 0). Its voltage cannot change abruptly.

## Slide 8: Capacitors
Example: Calculate the current through the capacitor C = 0.1μF with the voltage as shown: v(t) = 5(1 – e-t /10-6)

## Slide 9: Capacitors

## Slide 10: Capacitors in parallel
  Capacitors in parallel has an equivalent capacitance which can be represented sum of all individual capacitance:
C1
C2
C3
Cn
CN
Ceq

## Slide 11: Capacitors in series
  Capacitors in series has an equivalent capacitance which can be represented by:
Ceq
C1
∙ ∙ ∙
∙ ∙ ∙
C2
C3
Cn
CN

## Slide 12: Parallel and Series Capacitors
Example:
Determine the equivalent capacitance Ceq , C1 = 2mF, C2 = 2mF, C3 = 1mF, C4 = 1/3mF, C5 = 1/3mF, C6 = 1/3mF
C1
C2
C3
C4
C5
C6
Ceq

## Slide 13: Inductors
  An inductors is a coil of wire wound around a core.
  The core can be air, an insulator or ferromagnetic material.
An inductor is an electrical element designed to store energy.
core
Electrical Symbol

## Slide 14: Inductors
Given a current passes through an inductor, the voltage across the inductor is directly proportional to the rate of change of the current:
Inductance L depends on the number of turns N, the length of the inductor l, the cross sectional area of the core A and the permeability of the core m.
The inductance is measured in Henry (H).
where

## Slide 15: Inductors
The current-voltage relationship of an inductor:
The energy stored in an inductor:
An inductor is a short circuit in a steady state (i.e. di /dt = 0), its current cannot change abruptly.
initial current
at t = t0

## Slide 16: Inductors in series
  Inductors in series has an equivalent inductance which can be represented by sum of all individual inductance :
Leq
L1
∙ ∙ ∙
∙ ∙ ∙
L2
L3
Ln
LN

## Slide 17: Inductors in parallel
  Inductors in parallel has an equivalent inductance which can be represented by:
L1
L2
L3
Ln
LN
Leq

## Slide 18: Inductors in parallel and series
Example :
Calculate the equivalent inductance for the inductive
network in the circuit shown below:
Leq = 25mH

## Slide 19: RLC circuits at steady state
Find Vc and iL in the circuit at a steady state
Replace a capacitor by an open circuit
Replace an inductor by a short circuit

## Slide 20: RLC circuits at steady state
No current through 4W, so 4W can be ignored.
So i = iL
i = 12/(1+5) = 2A
iL = 2A
No current through 4W, so Va = Vc
Va = 12(5/6) = 10V
Vc = Va = 10V
va
vc
0V
Voltage across the capacitor is 10V