## Slide 1: AST10401 Introduction to Electrical Engineering
5. First Order Circuits

## Slide 2: First order circuits
A First Order Circuit is a circuit that contains a single energy storing element (either a capacitor or an inductor) together with a number of sources and resistors.
1st order
R1
R2
C
vs
+
–
Rs
R1
vs
+
–
L2
R2
L1
Not 1st order

## Slide 3: A first order circuit with switches
Assumption:
A first order circuit with a switch exists from a long time ago and the switch is activated (opened / closed) at t = 0 only.
3
R1
R2
C
vs
+
–
R3
The circuit exits for a long long time.

## Slide 4: A first order circuit with switches
If the circuit exists for a long time and the switch is activated only at t = 0, the circuit would have Two DC steady states:
  A DC steady state Just Before t = 0.
  A DC steady state Long After t = 0.
A DC steady state means there is no change in both voltages and currents in that circuit.

## Slide 5: Steady state Just Before t = 0
The circuit exists from a long time ago.
All voltages and currents settle down before t = 0.
Just Before t = 0 (denote as t = 0-), the circuit is in steady state.
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
t = 0- (the switch is not activated yet)
R3
t → - ∞ (a long long time ago)

## Slide 6: Steady state long after t = 0
The switch is closed at t = 0.
Long After t = 0 (t → ∞), all voltages and currents settle down again.
The circuit is in another steady state when t → ∞.
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
t → ∞
R3
t = 0

## Slide 7: A first order circuit with switches
We have two steady state circuits:
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
R3
The circuit at t = 0-
The circuit at t → ∞
(just before t = 0)
(long after t = 0)

## Slide 8: A first order circuit with switches
Each steady state has it own equivalent circuit.
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
R3
The equivalent circuit at t = 0-
The equivalent circuit at t → ∞
(just before t = 0)
(long after t = 0)

## Slide 9: Initial Conditions
The Initial Conditions of a capacitor :
Steady capacitor current or voltage just before t = 0 is
denoted as Ic(0–) and Vc(0–).
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
R3
The equivalent circuit at t = 0-

## Slide 10: Final Conditions
The Final Conditions of a capacitor :
Steady capacitor current or voltage long after t = 0 (t → ∞) is
denoted as Ic(∞) and Vc(∞).
R1
R2
C
vs
+
–
R3
R1
R2
C
vs
+
–
R3
The equivalent circuit at t → ∞

## Slide 11: DC Steady-State
Example:
Find the initial and final current of the inductor when is = 10mA.
is
t = 0
R
L
iL
a
b

## Slide 12: DC Steady-State
10mA
The circuit is in steady state at t = 0-
R
L
iL
iL
In DC steady state, inductors act like short circuits, thus no current flows through R.
a
b
10mA

## Slide 13: DC Steady-State
is
t = 0
R
L
iL
At t = 0, the inductor current cannot change instantaneously, the inductor keeps the same current flow at t = 0.
L
iL
R
a
b
By KCL

## Slide 14: DC Steady-State
Energy stored in the inductor is released to resistor R but the amount of energy is finite.
So, eventually, all energy stored are released to resistor R. In that case, no energy remains in the inductor. Hence iL(∞) = 0A at the end.
The circuit reaches another steady state when t → ∞
L
iL
R

## Slide 15
Step response of first order circuit

## Slide 16: Unit-Step Function
The unit step function u(t) is 0 for t < 0 and 1 for t ≥ 0.

## Slide 17: Unit-Step Function
An abrupt voltage change in a voltage source can be represented by a step function:
  a step voltage source
V0 u(t)
V0

## Slide 18: Unit-Step Function
An abrupt current change in a current source can be represented by a step function:
  a step current source
I0 u(t)
I0

## Slide 19: Step response of an RC circuit
Interested in knowing how v changes for t ≥ 0. (i.e. find v(t) for t ≥ 0)
Vs
Suppose before t = 0, the initial voltage of the capacitor is Vo.
We close the switch at t = 0, the capacitor will be charged up by the voltage source Vs. (This is called the Charging Process)
For t ≥ 0

## Slide 20: Step response of an RC circuit
The initial capacitor voltage at t = 0- : v(0-) = V0, So v(0) = v(0-) = V0
The final capacitor voltage at t → ∞ : v(∞) = Vs (as a cap is an open circuit at steady state)
V0
We expect a curve joining these two points.
We want to know how v changes with time.
Assume that Vs > V0

## Slide 21: Step response of an RC circuit
For t ≥ 0, apply KCL at a, we have
For t ≥ 0
Determine how v changes for t ≥ 0. (i.e. find v(t) for t ≥ 0)
a
Vs
Rearrange terms we have
set that node as ground
0V

## Slide 22: Step response of an RC circuit
Integrate both side,
For t ≥ 0
Recall that the initial voltage V0 on the capacitor
Vs
Thus

## Slide 23: Step response of an RC circuit
The time constant is
For t ≥ 0
Vs
This is called the step response of an RC circuit which is caused by a sudden change of the circuit configuration at t = 0.

## Slide 24: Step response of an RC circuit
Final value at t → ∞
Initial value at t = 0
final voltage
initial voltage
The capacitor voltage v(t) is given by
Assume that Vs > V0

## Slide 25: Step response of an RC circuit
Three steps to find the step response of an RC circuit (voltage across C):
Find the initial capacitor voltage v(0).
Find the final capacitor voltage v(∞):
Determine the time constant  = RC.
Put them in to the expression:
Vs
 can only be determined in “a standard form RC circuit”
A standard form RC circuit

## Slide 26: Step response of an RC circuit
Example: The switch has been in position A for a long time. At t = 0, the switch moves to B. Determine v(t) for t ≥ 0.
For t = 0-, the capacitor acts like an open circuit (v is the same as the voltage across 5k), so
But capacitor voltage cannot change instantly. Thus,

## Slide 27: Step response of an RC circuit
For t ≥ 0, the switch is at position B, find the resistance experienced by the 0.5mF capacitor:
The time constant is
Since the capacitor acts like an open circuit at steady state. So,
“A standard form RC circuit”
Vs
For t ≥ 0

## Slide 28: Natural response of RC circuit
When an RC circuit is connected no source after t = 0 (i.e. final cap. voltage v(∞) = 0), the step response of the RC circuit in this special case is given by
The voltage response of the RC circuit is an exponential decay of the initial voltage v(0).
The response is due to the initial energy stored in the cap.
It is also known Natural Response of an RC circuit.

## Slide 29: Natural response of RC circuit
Example
The switch has been closed for a long time and it is opened at t = 0, find v(t) for t ≥ 0
For t < 0, the capacitor is an open circuit
Voltage across a capacitor cannot change instantly, so
Cap. Voltage just before t = 0
t = 0-

## Slide 30: Natural response of RC circuit
Req
The time constant is
The voltage v(t) across the capacitor for t ≥ 0 is
For t ≥ 0, the circuit connects no source.
“a standard form RC circuit without a source (Vs = 0)”
Vs

## Slide 31: Step response of an RL circuit
Vs
For t ≥ 0
Suppose before t = 0, the initial current of an inductor is I0.
We close the switch at t = 0, the inductor is power supplied by the voltage source Vs.
I0
Interested in knowing how i changes for t ≥ 0. (i.e. find i(t) for t ≥ 0)

## Slide 32: Step response of an RL circuit
The initial inductor current at t = 0- : i(0-) = Io, So i(0) = i(0-) = Io
The final inductor current at t → ∞: i(∞) = Vs/R (as an inductor is an short wire at steady state)
We expect a curve joining these two points.
We want to know how i changes with time
Assume that I0 > Vs /R

## Slide 33: Step response of an RL circuit
For t ≥ 0, by KVL, we have
Determine how i changes for t ≥ 0. (i.e. find i(t) for t ≥ 0)
For t ≥ 0
Vs
0V
0V
i

## Slide 34: Step response of an RL circuit
Integrate both side, we have
For t ≥ 0
Vs
Recall that the initial current,

## Slide 35: Step response of an RL circuit
The time constant is
For t ≥ 0
Vs
This is called the step response of an RL circuit which is caused by a sudden change of the circuit configuration at t = 0.

## Slide 36: Step response of an RL circuit
Final value at t → ∞
Initial value at t = 0
final current
Initial current
The inductor current i(t) is given by
Assume that I0 > Vs /R

## Slide 37: Step response of an RL circuit
Three steps to find the step response of an RL circuit (current of L):
Find the initial inductor current i(0) at t = 0
Find the final inductor current i(∞)
Determine the time constant  = L/R.
Put them in to the expression:
 can only be determined in “A standard form RL circuit”
A standard form RL circuit
Vs

## Slide 38: Step response of an RL circuit
Example: Find i(t) for t ≥ 0. Assume that the switch has been closed for a long time before t = 0.
When t = 0-, the current through the inductor (short circuit) is
When switch is opened for a long time, the current through the inductor (short circuit) is
The total resistance experienced by the inductor is
Vs
a standard form RL circuit

## Slide 39: Step response of an RL circuit
The time constant is
Thus
Vs
a standard form RL circuit

## Slide 40: Natural response of RL circuit
When an RL circuit is connected no source after t = 0 (i.e. final inductor current i(∞) = 0), the step response of the RL circuit in this special case is given by
The current response of the RL circuit is an Exponential Decay of the initial inductor current i(0).
The response is due to the initial energy stored in the inductor.
It is also known Natural Response of an RL circuit.

## Slide 41: Natural response of RL circuit
The switch has been closed for a long time. At t = 0, the switch is opened. Calculate i(t) for t ≥ 0.
When t < 0 the switch is closed, the inductor is a short circuit.
By current divider,
t = 0-

## Slide 42: Natural response of RL circuit
Since the current through an inductor cannot change immediately
When t ≥ 0, the circuit connects no source.
The equivalent resistance experienced by the inductor is
The time constant is
Thus
t ≥ 0