## Slide 1: Chapter 8 Analog-to-Digital Converter (ADC)

## Slide 2: Why Analog-to-Digital Conversion?
In the physical world, everything is analog (continuous).
We need an analog-to-digital converter to translate analog signals to digital numbers so that the microcontroller can read and process them.

## Slide 3: Example: 2-bit ADC

## Slide 4: n-resolution ADC
 | Analog voltage (V) | Digital represen-tation
VREF- | 0 | 0
VREF+ | VDD | 2n-1
Vk |  | k
Or in terms of VREF- & VREF+:
Notes: The output characteristic of an ideal AID converter using n bits to represent the conversion result is shown. An n-bit A/D converter has 2^n possible output code values.
For a n-resolution ADC, there are in total 2^n levels. ADC conversion requires a negative voltage reference and a positive voltage reference. Level 0 represents the negative voltage reference and Level 2^n-1 represents the positive voltage reference. So we would ask, what voltage does Level k represent? Between Level 0 and 2^n-1, we have 2^n-1 intervals. Each interval represents Vdd/2^n-1 voltages. We are in Level k, Level k represents Vk

## Slide 5: Examples
e.g., VREF- = 0, VREF+ = 5V, 10-bit resolution ADC. Suppose the ADC results are as follows. What are the corresponding voltages?
20
  V20 = 20x5/(210-1) = 0.0977V
499
  V499 = 499x5/(210-1)= 2.43V
898
  V898 = 898x5/(210-1)=4.38V

## Slide 6: How can ADC be done?
Successive Approximation

## Slide 7: Examples of Successive Approximation

## Slide 8: PIC18 ADC Module
Notes: There is one ADC module in PIC18.
minimum resolution is Vref+-Vref-/4095

## Slide 9: Block Diagram of PIC18 ADC

## Slide 10: SFR involving in ADC
A/D Control Register 0 (ADCON0)
A/D Control Register 1 (ADCON1)
A/D Control Register 2 (ADCON2)
A/D Result High Register (ADRESH)
A/D Result Low Register (ADRESL)

## Slide 11: ADCON0

## Slide 12: ADCON0
CHS3:CHS0: Analog Channel Select Bits
  PIC18F4520 has only 1 Analog-to-Digital unit
  Can only select 1 input from AN0:AN12 to be sampled and converted
GO/DONE:
  Setting this bit starts A/D conversion
  Cleared when A/D conversion is done
ADON:
  Power up (1)/Shut off (0) the ADC module

## Slide 13: ADCON1

## Slide 14: ADCON1
Voltage Reference Configuration bits
VCFG1: VREF- source
  1 = VREF- (AN2)
  0 = VSS
VCFG0: VREF+ source
  1 = VREF+ (AN3)
  0 = VDD
A/D Port Configuration bits
PCFG<3:0> – The input analog signal must be configured as an analog input.

## Slide 15: ADCON1: A/D Port Configuration bits

## Slide 16: ADCON1: A/D Port Configuration bits
Do the following two lines sound familiar?
movlw 0x0F
movwf ADCON1
Notes: You set all AN channels to be digital in all your lab exercises. Pins in microcontroller are multiplexed for different purposes. For example, Pin 2 is both analog channel 0 and 0 pin of PORT A. In all your labs, pin are used for digital I/O. That’s why you should set the last 4 bits of ADCON1 to be 1111.

## Slide 17: ADCON2

## Slide 18: ADCON2
ADFM: A/D Result Format Select bit
Notes: You have two bytes to store the result of the conversion. Two bytes have 16-bit but the result of the A/D conversion is only 10 bits. You can choose to display the result as right or left justified.

## Slide 19: A/D Conversion Time: TAD
TAD = time required to complete 1-bit A/D conversion
Time required for one full 10-bit A/D conversion is 11 to 12 TAD – Successive approximation
From the PIC18F4520 specification, TAD must be between 0.7 – 25 μs.
TAD can be specified from 2Tosc to 64Tosc by selecting the A/D Conversion Clock Select Bits (ADCS<0:2> in ADCON2).

## Slide 20: How should TAD be set?
e.g., If a 4MHz clock is installed, Tosc = 0.25μs.
The minimum TAD that can be set is 4Tosc.
TAD can be chosen from 4Tosc (1μs) to 64Tosc (16μs).

## Slide 21: Sample-and-hold circuit
The analog input voltage will charge up CHOLD to a steady state before ADC begins.
The time required to reach steady state depends on Rs, RIC, Rss and CHOLD.
Notes: In order to ensure that the analog input voltage is stable throughout the A/D conversion process, PIC18 has a sample and hold circuit. The capacitor holds the voltage to be converted into digital code. The charge-holding capacitor must be allowed to fully charge to the input channel voltage level.

## Slide 22: A/D Acquisition Time (ACQT)
The minimum acquisition time (TACQ) for PIC18F4520 is 1.4μs.
ADC module will insert an acquisition time between the GO/DONE bit is set and when the conversion starts.
Suppose TAD = 1μs. TACQ >= 2 TAD
TACQ is set by setting ACQT<0:2> of ADCON2 (chosen as a multiple of TAD).

## Slide 23: A/D Conversion Process
Set GO/DONE bit
Wait TACQ to charge up CHOLD
CHOLD is disconnected and ADC begins
11-12 TAD is required for a 10-bit ADC
When finished:
  ADRESH:ADRESL are loaded
  GO/DONE bit is cleared
  ADIF bit is set
  CHOLD is reconnected to the analog input

## Slide 24: Example Use of the ADC
Main: movlw b'00001110' movwf ADCON1 movlw b'00000001' movwf ADCON0 movlw b'00010100' movwf ADCON2 clrf TRISD MainLoop: bsf ADCON0, GO adc_wait: btfsc ADCON0, GO bra adc_wait movff ADRESH, PORTD bra MainLoop | ;Set RA0 Analog Port, others Digital I/O ;Select ADC Channel 0, Enable ADC ; ADFM Left justified, ACQT 4TAD, FOSC/4 ; set PORTD output ; start Conversion ; adc_wait;wait ADC to be done ;display Top 8 bit

## Slide 25: Example
Assume fOSC = 4MHz, write a few
instructions to turn on and configure a PIC
ADC with the following requirements:
ADC converts the analog signal fed into Channel AN3.
ADC result is left justified.
Select VDD and VSS as reference voltages.
TAD must be at least 2.5 μs.
TACQ must be at least 18 μs.

## Slide 26: Example

## Slide 27: You should be able to ...
Describe the roles of the following 5 registers: ADCON0, ADCON1, ADCON2, ADRESH and ADRESL in the A/D conversion. These registers specify the following options:
  Which channel to convert?
  Which channel should be set to accept analog input?
  How to store the conversion result?
  What is Vref+ and Vref-?
  What is the conversion time (TAD)?
  What is the acquisition time (TACQ)?

## Slide 28: You should be able to ...
Explain the process of sampling analog voltage before A/D conversion.
Explain why an acquisition time is needed before A/D conversion.
Describe the successive approximation algorithm.
Describe the whole A/D conversion process.